## Slide 1: EE2026 Digital Design
Chua Dingjuan elechuad@nus.edu.sg

## Slide 2: Module Outline
  Part 1
    Number systems
    Boolean Algebra and logic gates
    Gate-level design and minimization
    Combinational logic circuits and design
    Logic IC family
  Part 2
    Sequential logic circuits
      Flip-Flops, Counters, (Shift Registers)
    Verilog review
    Verilog behavioral and structural modeling
    Digital finite state machine design
    Modeling of FSMs using Verilog

## Slide 3: Expected Learning Outcomes
– Able to design basic sequential logic circuits using flip-flops. – Able to design, build and test digital systems using FPGAs. – Able to design, model and simulate digital logic circuits using Verilog.
– Able to design and model simple state machines based on the FSM approach.

## Slide 4: Module Organization
10-12 Lectures (2+1 hours / week)
5 Tutorial Sessions
Assessment
  Weekly Quizzes – 5%
  Luminus Quiz (MCQ, MRQ, FIB), three attempts.
  Due Sunday of the following week. Eg. W6 quiz is due recess week Sunday.
  Final Quiz – 15%
  Week 13 (Venue & Time to be confirmed)

## Slide 5: EE2026 Tutorial & Lab Schedule
Week | Tutorials | Lab | Quiz
WK 6 | -- |  | 
Recess Week |  |  | 
WK7 | Tutorial – 6 | Project Lab 1 | 
WK8 | Tutorial – 7 | Project Lab 2 | 
WK9 | Tutorial – 8 | Project Lab 3 | 
WK10 | Tutorial – 9 | Project Lab 4 | 
WK11 | Tutorial – 10 |  | 
WK12 |  | Project Lab 5 / Project Evaluation | 
WK13 |  |  | Final Quiz

## Slide 6: SEQUENTIAL CIRCUITS - I
©Copyright CHUA DINGJUAN. All rights reserved.

## Slide 7: Design a circuit to do this >>
When the button is pushed :
Turn On the light if it is Off
Turn Off the light if it is On
What is missing?
Remembering the previous state of the bulb  MEMORY
Responding to an input EVENT (cf. input value)


## Slide 8: Sequential Logic Circuits?
Combinational Logic Circuits:
Outputs depend on current inputs
Sequential Logic Circuits:
Outputs depend on current and previous inputs  Memory!
Requires separation of previous, current, future : states
2 Types of sequential circuits:
Synchronous | Asynchronous
Clocked: need a clock input | Unclocked
Responds to inputs at discrete time instants governed by a clock input | Responds whenever input signals change

## Slide 9: SR Flip-flop (FF)
The simplest memory element has two stable states : Flip-Flop (FF)  it can store 1 bit of information
Most basic FF : Set-Reset (SR) Flip-flop / Latch
S
R
Q
__Q
Implemented with NOR / NAND gates
S | R | Output | Q+
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
0 0 is the rest state |  |  | 

## Slide 10: SR Flip-flop (FF)
S | R | Output Q
0 | 0 | 
0 | 1 | Q = 0
1 | 0 | 
1 | 1 | 
S
R
Q
__
Q
A | B | NOR

NOR Implementation

## Slide 11: SR Flip-flop (FF)
S
FF can record and store transient events.
Switching is not instantaneous  propagation delays
1) Assume that the rest state is: S = R = 0; let = 0, = 1
S | R | Output
0 | 0 | Hold
0 | 1 | Q = 0
1 | 0 | Q = 1
1 | 1 | Invalid
0 0 is the rest state |  | 
2) If S while R = 0  = 1, = 0, i.e., the event (S going high) is recorded and stored as = 1.
R
Q
_ Q

## Slide 12: A Simple Application…
Mechanical switches bounce before settling down which may cause problems as inputs.
Switch debouncing is a common use of S-R FFs.
close
(bounce)
open
(bounce)
VCC
(a) Output of typical mechanical switch
(b) Debounced switch output signal
S | R | Output
0 | 0 | Hold
0 | 1 | Q = 0
1 | 0 | Q = 1
1 | 1 | Invalid
0 0 is the rest state |  | 

## Slide 13: JK FF
The JK FF is a synchronous circuit:
The JK FF is based on SR with 2 improvements : _____ & ______
J
K
Q
_Q
CLK | J | K | Q+
 | 0 | 0 | Q
 | 0 | 1 | 0
 | 1 | 0 | 1
 | 1 | 1 | 
CLK | J | K | Q+
 | 0 | 0 | Q
 | 0 | 1 | 0
 | 1 | 0 | 1
 | 1 | 1 | 
Clock input is a controlling input. It specifies when circuit read inputs / change outputs.
Synchronous circuits respond only at the _______ clock edges i.e., LOW  HIGH, HIGH  LOW transitions
At any other time, changing inputs have no effect on the output.
rising falling
edge edge
CLK | J | K | Q | Q+
 | 0 | 0 | 0 | 0
 | 0 | 0 | 1 | 1
 | 0 | 1 | 0 | 0
 | 0 | 1 | 1 | 0
 | 1 | 0 | 0 | 1
 | 1 | 0 | 1 | 1
 | 1 | 1 | 0 | 1
 | 1 | 1 | 1 | 0
Hold
Clear
Set
Toggle
characteristic table
condensed characteristic table

## Slide 14: Respond @ Active Clock Edges
1
J
0
1
K
0
1 hold clear hold set toggle
Q/Q+
0 tpHL tpLH
When inputs don’t change  FF outputs don’t change.
If inputs change  FF output changes state only at active clock edge.
Ti Ti+1 Ti+2 Ti+3 Ti+4 Ti+5
CLK
tsetup
?

## Slide 15: FF Timing Parameters
tsetup : minimum time before the active clock edge by which FF inputs must be stable.
thold: minimum time inputs must be stable after active clock edge
tpHL : time taken for FF output to change state from High to Low.
tpLH : time taken for FF output to change state from Low to High.
clock
tsetup
thold
What happens if inputs change state right at the active clock transition? Answer: output is _________________
Thus, input changes must meet required setup & hold times of device == Operating Speed of device
http://www.ti.com/product/SN74LS107A

## Slide 16: Commercially Available JK FFs
J Q
K _
Q
CLR
PR
J Q
K _
Q
CLR
74’107 with asynchronous clear
CLK | PR | CLR | J | K | Q+
X | L | H | X | X | H
X | H | L | X | X | L
X | L | L | X | X | not allowed
 | H | H | L | L | Q
 | H | H | L | H | L
 | H | H | H | L | H
 | H | H | H | H | 
CLK | PR | CLR | J | K | Q+
X | L | H | X | X | H
X | H | L | X | X | L
X | L | L | X | X | not allowed
 | H | H | L | L | Q
 | H | H | L | H | L
 | H | H | H | L | H
 | H | H | H | H | 
74’109 with direct set & direct clear
CLK | CLR | J | K | Q+
X | L | X | X | L
 | H | L | L | Q
 | H | L | H | L
 | H | H | L | H
 | H | H | H | 
74’107
74’109

## Slide 17: Other Flip-Flops…
D Q
_
EN Q
D Q
_
Q
D Flip-Flop
CLK | D | Q+
 | 0 | 0
 | 1 | 1
T Q
_
Q
T Flip-Flop
CLK | T | Q+
 | 0 | Q
 | 1 | 
CLK | T | Q+
 | 0 | Q
 | 1 | 
J Q
K
_
Q
T
CLK
A T Flip-flop made from a J-K Flip-flop
CLK | J | K | Q+
 | 0 | 0 | Q
 | 0 | 1 | 0
 | 1 | 0 | 1
 | 1 | 1 | 
CLK | J | K | Q+
 | 0 | 0 | Q
 | 0 | 1 | 0
 | 1 | 0 | 1
 | 1 | 1 | 
Since T Flip-flops are easy to construct from other FFs, they are not available commercially.
D Latch
EN | D | Q+
0 | X | No change
1 | 0 | 0
1 | 1 | 1

## Slide 18: Verilog Time! – D-FF
CLK | D | Q+
 | 0 | 0
 | 1 | 1
D
Q
CLK
D
Q

## Slide 19: Verilog Time! – D-FF
CLK | D | Q+
 | 0 | 0
 | 1 | 1
D
Q
module dff ( input
output );
endmodule
always @ (posedge __)
always @ (negedge __)
always @ (posedge clock)
begin
end



## Slide 20: Some notes on: always & reg
Registers
Anything assigned in an always block must be type reg
In Verilog, the term register (reg) simply means a variable that can hold a value
Values of registers can be changed instantaneously. This is different from the wire type!
Always Block
Conceptually, the always block runs once when a signal in sensitivity list changes value.
Statements within always block are executed sequentially.
begin and end behave like parentheses/brackets
No assign!

## Slide 21: Summary
SR Flip Flop & Applications
JK Flip Flop
FF Timing Parameters
Commercial JK Flip Flops
Verilog description of D Flip Flop

## Slide 22: Practice Question
CLK
Q
Q
Given the circuit diagram below, complete the timing diagram below by filling in Q and Q. Assume that the initial value of Q is ‘0’ and include all propagation delays.
D
Q
Q
CLK